## Slide 1: IPv6: Are we really ready to turn off IPv4?
Geoff Huston
APNIC

## Slide 2: The IPv6 Timeline…
1990
2000
2010
2020
1989- Forecasts of IPv4 Address Exhaustion
1993 - Next Generation IP work in the IETF
1995 IPv6 Spec (RFC1883)
IPv4 Address Exhaustion
1996 - 6Bone Testbed (1996 – 2006)
1999 - RIR Allocations of Unicast IPv6 start
2003 - Dual Stack Transition underway

## Slide 3: The IPv6 Timeline…
1990
2000
2010
2020
1989- Forecasts of IPv4 Address Exhaustion
1993 - Next Generation IP work in the IETF
1995 IPv6 Spec (RFC1883)
IPv4 Address Exhaustion
1996 - 6Bone Testbed (1996 – 2006)
1999 - RIR Allocations of Unicast IPv6 start
2003 - Dual Stack Transition underway
Yes, we’ve been working on this for close to 30 years!

## Slide 4
In-situ transition…

## Slide 5
In-situ transition…
IPv4 Internet
Phase 1 – Early Deployment
Edge Dual -Stack Networks
IPv6 networks interconnect by
IPv6-over-IPv4 tunnels

## Slide 6
In-situ transition…
Phase 2 – Dual Stack Deployment
Edge Dual-Stack
Networks
IPv6 networks interconnect by
Dual Stack transit paths
Transit Dual-Stack
Networks

## Slide 7
In-situ transition…
IPv6 Internet
Phase 3 – IPv4 Sunset
Edge Dual Stack Networks
IPv4 networks interconnect by
IPv4-over-IPv6 tunnels

## Slide 8
In-situ transition…
IPv4 Pool Size
IPv6 Deployment
Size of the Internet
Dual Stack Transition
We’re pretty lousy at following plans!

## Slide 9
The Map of IPv6 penetration – November 2017

## Slide 10
The Map of IPv6 penetration – November 2017

## Slide 11
We’re stuck in Phase 2
Some 15% - 20% of Internet users have IPv6 capability
In the IoT world the IPv6 numbers appear to be far lower than this
Most new IP deployments use IPv6+ (NATTED) IPv4
IPv4-only Legacy networks are being (gradually) migrated to dual stack

## Slide 12
We’re stuck in Phase 2
Some 15% - 20% of Internet users have IPv6 capability
In the IoT world the IPv6 numbers appear to be far lower than this
Most new IP deployments use IPv6+ (NATTED) IPv4
IPv4-only Legacy networks are being (gradually) migrated to dual stack
The current situation is that the universal “glue” of the Internet remains IPv4, while IPv6 is still an optional feature!

## Slide 13
Today
We appear to be in the middle of the transition!
Dual Stack networks cannot drop support for IPv4 as long as significant services and user populations do not support IPv6

## Slide 14
Today
We appear to be in the middle of the transition!
Dual Stack networks cannot drop support for IPv4 as long as significant services and user populations do not support IPv6 – and we can’t tell when that may change
Nobody is really in a position to deploy a robust at-scale ipv6-only network service today, even if they wanted to!
And we are not even sure if we can!

## Slide 15
Today
We appear to be in the middle of the transition!
Dual Stack networks cannot drop support for IPv4 as long as significant services and user populations do not support IPv6 – and we can’t tell when that may change
Nobody is really in a position to deploy a robust at-scale ipv6-only network service today, even if they wanted to!
And we are not even sure if we can!

## Slide 16
The Issue
  We cannot run Dual-Stack services indefinitely
  At some point we need to support networks that only have IPv6
  Is that viable?

## Slide 17
In other words…
What do we rely on today in IPv4 that does not appear to have a clear working counterpart in IPv6?

## Slide 18
In other words…
What do we rely on today in IPv4 that does not appear to have a clear working counterpart in IPv6?
If the answer is “nothing” then we are done!
But if there is an issue here, then we should be working on it!

## Slide 19
Version
IHL
Total Length
Flags
Identification
Fragment Offset
Time To Live
Source Address
Destination Address
Options
Padding
Protocol
Header Checksum
Type of Service
Version
Class
Flow
Payload Length
Hop Limit
Source Address
Destination Address
Next Header
IPv4 Header
IPv6 Header
IPv6: What changed?

## Slide 20
IPv6: What changed?
Type of Service is changed to Traffic Class
32 bit Fragmentation Control were pushed into an Extension Header
Flow Label Added
Options and Protocol fields replaced by Extension Headers
Checksum becomes a media layer function

## Slide 21
IPv6: What changed?
Type of Service is changed to Traffic Class
32 bit Fragmentation Control were pushed into an Extension Header
Flow Label Added
Options and Protocol fields replaced by Extension Headers
Checksum becomes a media layer function

## Slide 22
IPv6: What changed?
Type of Service is changed to Traffic Class
32 bit Fragmentation Control were pushed into an Extension Header
Flow Label Added
Options and Protocol fields replaced by Extension Headers
Checksum becomes a media layer function
The only substantive changes with IPv6 are:
- the handling of fragmentation via Extension Headers
- cementing the Don’t’Fragment bit to ON for routers

## Slide 23
IPv4 Router
IPv4 header
Payload
TCP/UDP header
IPv4 header
Payload
TCP/UDP header
1
2
IPv6: What changed?
IPv4 “Forward Fragmentation”

## Slide 24
IPv4 Router
IPv4 header
Payload
TCP/UDP header
IPv4 header
Payload
TCP/UDP header
IPv6 Router
IPv6 header
Payload
TCP/UDP xtn header
Payload
TCP/UDP xtn header
ICMPv6 PTB
IPv6 header
IPv6 header
Payload
TCP/UDP xtn header
Fragmentation xtn header
1
2
3
1
2
IPv6: What changed?
IPv4 “Forward Fragmentation”
IPv6 “Source Fragmentation”
Source
Source

## Slide 25: ICMPv6 and Anycast
Sender Instance
Client
Sender Instance
Sender Instance
Anycast Constellation
Sender Instance
Sender Instance
It is not obvious (or even assured) that every router on the path from an anycast instance to a client host will necessarily be part of the same anycast instance “cloud”
The implication is that in anycast, the reverse ICMPv6 PTB messages will not necessarily head back to the original sender!

## Slide 26
New Dependencies
For IP fragmentation to work in IPv6 then:
- all ICMPv6 messages have to be passed backwards from the interior
of the network to the sender
- IPv6 packets containing a IPv6 Fragmentation Extension
header should not be dropped

## Slide 27
Processing incoming ICMPv6 messages
Only the sending host now has control of fragmentation – this is a new twist
A received ICMPv6 message needs to alter the sender’s state to that destination
For TCP, if the ICMP payload contains the TCP header, then you can pass this to the TCP control block. TCP can alter the session MSS and resend the dropped data
For UDP – um, err, um well

## Slide 28
Processing incoming ICMPv6 messages
Only the sending host now has control of fragmentation – this is a new twist
A received ICMPv6 message needs to alter the sender’s state to that destination
For TCP, if the ICMP payload contains the TCP header, then you can pass this to the TCP control block. TCP can alter the session MSS and resend the dropped data
For UDP – um, err, um well
Maybe you should store the revised path MTU in a host forwarding table cache for a while
If you ever need to send another UDP packet to this host you can use this cache entry to guide your fragmentation behaviour

## Slide 29
IPv6 and Fragmentation
The theory is that TCP in IPv6 should never send a fragmented packet - TCP should use the session MSS as a guide to packet sizes and segment the stream according to the session MSS
However, UDP cannot avoid fragmentation - large payloads in UDP simply need to be fragmented to fit within the path MTU
    Fragmentation in IPv6 uses the same control fields as IPv4 – a packet identifier, a fragmentation offset and a More Frags flag
    BUT they are located in an inserted “shim” that sits between the IPv6 packet header and the UDP transport header - this is an instance of the IPv6 “Extension Header”

## Slide 30
IPv6 Fragmentation Extension Header Handling
The extension header sits between the IPv6 packet header and the upper level protocol header for the leading fragged packet, and sits between the header and the trailing payload frags for the trailing packets
Practically, this means that transport-protocol aware packet processors/switches need to decode the extension header chain, if its present, which can consume additional cycles to process/switch a packet – and the additional time is not predictable. For trailing frags there is no transport header!
Or the unit can simply discard all Ipv6 packets that contain extension headers!
Which is what a lot of transport protocol sensitive IPv6 deployed switching equipment actually does (e.g. load balancers!)
IPv6 header
Payload
TCP/UDP xtn header
Fragmentation xtn header

## Slide 31
IPv6 Fragmentation Extension Header Handling
There is a lot of “drop” behaviour in the IPv6 Internet for Fragmentation Extension headers
RFC7872 – recorded drop rates of 30% - 40%
This experiment sent fragmented packets towards well-known servers and observed whether the server received and reconstructed the fragmented packet
But sending fragmented queries to servers is not all that common – the reverse situation of big responses is more common
So what about sending fragmented packets BACK from servers – what’s the drop rate of the reverse case?

## Slide 32
IPv6 Fragmentation Extension Header Handling
We used an ad-based measurement system, using a custom packet fragmentation wrangler as a front end to a DNS and Web server to test IPv6 fragmentation behaviour
Client
DNS Resolver
IPv6 DNS Server
IPv6 NGINX Server
IPv6 ‘Fragmenter’
DNS Goo

## Slide 33
We used an ad-based measurement system, using a custom packet fragmentation wrangler as a front end to a DNS and Web server to test IPv6 fragmentation behaviour
IPv6 Fragmentation Extension Header Handling
Client
DNS Resolver
IPv6 ‘Fragmenter’
DNS Goo
We use a technique of “glueless” delegation and fragmentation of the NS query response to allow us to detect if the DNS resolver received the fragmented response
We track TCP ACKs at the server to see if the client received the fragmented TCP response
Client
DNS Resolver
IPv6 DNS Server
IPv6 NGINX Server

## Slide 34
IPv6 Fragmentation Extension Header Handling
Our Experiments were run across some 40M individual sample points in August 2017:
  37% of end users who used IPv6-capable DNS resolvers could not receive a fragmented IPv6 DNS response

## Slide 35
IPv6 Fragmentation Extension Header Handling
Our Experiments were run across some 40M individual sample points in August 2017:
  37% of end users who used IPv6-capable DNS resolvers could not receive a fragmented IPv6 DNS response
  20% of IPv6-capable end users could not receive a fragmented IPv6 packet

## Slide 36
IPv6 Fragmentation is very unreliable
Why don’t we see this unreliability in today’s IPv6 networks affecting user transactions?

## Slide 37
IPv6 Fragmentation is very unreliable
Why don’t we see this unreliability in today’s IPv6 networks affecting user transactions?
Because IPv4 papers over the problem!

## Slide 38
IPv6 Fragmentation is very unreliable
Why don’t we see this unreliability in today’s IPv6 networks affecting user transactions?
Because IPv4 papers over the problem!
In a Dual-Stack environment there is always the option to flip to use IPv4 if you are stuck with Ipv6.
  The DNS does this, and Happy Eyeballs does this
So there are few user-visible problems in a dual stack environment
This means that there is no urgent imperative to correct these underlying problems in deployed IPv6 networks

## Slide 39
IPv6 Fragmentation is very unreliable
Why don’t we see this unreliability in today’s IPv6 networks affecting user transactions?
Because IPv4 papers over the problem!
In a Dual-Stack environment there is always the option to flip to use IPv4 if you are stuck with Ipv6.
  The DNS does this, and Happy Eyeballs does this
So there are few user-visible problems in a dual stack environment
This means that there is no urgent imperative to correct these underlying problems in deployed IPv6 networks
There is little in the way of practical incentives to fix this today!

## Slide 40
Living without IPv6 Fragmentation
If we apparently don’t want to fix this, can we live with it?
We are living with it in a Dual Stack world, because IPv4 just makes it all better!
But what happens when there is no IPv4 left?

## Slide 41
Living without IPv6 Fragmentation
If we apparently don’t want to fix this, can we live with it?
We are living with it in a Dual Stack world, because IPv4 just makes it all better!
But what happens when there is no IPv4 left?
TCP can work as long as IPv6 sessions use conservative MSS sizes
UDP can work as long as UDP packet sizes are capped so as to avoid fragmentation
We have to avoid IPv6 Fragmentation!

## Slide 42
Living without IPv6 Fragmentation
TCP can work as long as IPv6 sessions use conservative MSS sizes
UDP can work as long as UDP packet sizes are capped so as to avoid fragmentation
We have to avoid IPv6 Fragmentation!
Who needs to use large UDP packets anyway?

## Slide 43
Living without IPv6 Fragmentation
TCP can work as long as IPv6 sessions use conservative MSS sizes
UDP can work as long as UDP packet sizes are capped so as to avoid fragmentation
We have to avoid IPv6 Fragmentation!
Who needs to use large UDP packets anyway?
DNSSEC!

## Slide 44: What can we do about it?
A. Get all the deployed routers and switches to deliver ICMPv6 packets and accept packets with IPv6 Fragmentation Headers

## Slide 45: What can we do about it?
B. Get all the deployed routers and switches to alter the way IPv6 manages packet fragmentation

## Slide 46: What can we do about it?
C. Move the DNS off UDP

## Slide 47: Pick one?
All of these options have a certain level of pain, cost and potential inconvenience
Its hard to work out what is the best course of action, but it seems like a lot of extra effort if we take on all three at once!

## Slide 48: For TCP …
Working around this issue in TCP can be as simple as a very careful selection of a default IPv6 TCP MSS
  Large enough enough to offer a tolerable data carriage efficiency
  Small enough to avoid Path MTU issues
And perhaps you might want to to support TCP path MTU discovery (RFC 4281)

## Slide 49: For TCP …
But you have to take into account the observation that Path MTU discovery without reliable ICMPv6 signaling takes a number of Round Trip Times (delay)
And time is something no application designer has enough of to waste on probing path characteristics
So choose your TCP MSS very carefully
Hint: Smaller TCP MSS sizes are Better in IPv6!

## Slide 50: For UDP …
Working around this issue can be challenging with UDP
  ICMPv6 Packet Too Big filtering causes silence
  Fragment drop is silent drop
    Which means that protocols need to understand timeouts
An effort to work around this necessarily involves application-level adaptation to pass large responses without relying on UDP packet fragmentation

## Slide 51: If we can’t fix IPv6
And we can’t fix end-to-end transport
Then all that’s left is to look at the application protocol and see if we can re-define the protocol behaviour in a way eliminates fragmentation behaviour

## Slide 52: “Old Style” DNS
The original DNS protocol had this behaviour
  If the DNS payload was <= 512 bytes send the answer over UDP
  Otherwise send as much as will fit in 512 bytes set the truncate bit
  The receiver is meant to re-query using TCP upon receipt of a truncated response
Why did we change this behaviour?
Because we thought that fragmentation was “safe” and TCP was too costly
So we added Extension options for DNS to signal it was OK to send large fragmented UDP responses
But its not OK

## Slide 53: Large DNS Responses and IPv6
Change the protocol behaviour?
  Shift Additional Records into additional explicit UDP query/response transactions rather than bloating the original DNS response
  Perform UDP MTU discovery using EDNS(0) UDP Buffer Size variations as a probe
  Add a truncated minimal UDP response to trail a fragmented response (ATR)
Change the transport?
  DNS over TCP by default
  DNS over TLS over TCP by default
  DNS over QUIC
  Devise some new DNS framing protocol that uses multiple packets instead of fragmentation

## Slide 54: Where now?
We have a decent idea of the problem space we need to resolve
We’d prefer a plan that allows each of us to work independently rather than a large scale orchestrated common change
We’re not sure we can clean up all the ICMPv6 filters and EH packet droppers in the IPv6 network
And it sure seems a bit late in the day to contemplate IPv6 protocol changes
Which means that we are probably looking at working around the problem by changing the behaviour of applications

## Slide 55: What do the RFC’s say?

## Slide 56: What do the RFC’s say?

## Slide 57: What do the RFC’s say?

## Slide 58: What do the RFC’s say?

## Slide 59: What do the RFC’s say?
This BCP is saying that using EDNS(0) in the DNS to signal the capability of accepting large fragmented DNS responses was unwise, and if a host/application does know the path MTU, it should truncate at UDP at 1280 octets (and IPv4 should truncate at 512 octets!)

## Slide 60: But would that be enough?
Is the root cause problem with the way our IPv6 networks handle Fragmented IPv6 packets?
Or with the way our IPv6 networks handle IPv6 packets with Extension Headers?
The data presented here suggests that EH drop could be the underlying significant issue here
Perhaps we might want to think about advice to host stacks and applications to avoid EH altogether!
  Including fragmentation!

## Slide 61: What was the question again?
Oh yes, that’s right:
  “Are we ready for an IPv6-only Internet?”
  It appears that the answer is “no, not if we want the DNS to work!”

## Slide 62: What was the question again?
Oh yes, that’s right:
  “Are we ready for an IPv6-only Internet?”
  It appears that the answer is “no, not if we want the DNS to work!”
IPv6 Grade: B-
It’s close, but more effort is needed if you want to properly finish this work!

## Slide 63
Thanks!